## Slide 1: Red Planet Recycle
Meeting
29/11/2011

## Slide 2: Meeting Agenda
Discussion of Recycling Processes
Water
Biomass
Waste
Thermal
Air
Food
Potential Process Selection
Additional Questions
Task assignment for the Festive Period
Election of new Chairman and Secretary

## Slide 3: Water Recycling Processes
Gareth Herron
Sam Walpole

## Slide 4: General Technologies
Biological Tech
Digestion
Bio-Reactor Systems
Fermentation
EcocycLET Systems
Bioremediation
Membrane Seperations
Chemical Tech
Advanced Oxidation Processes
Electrocoagulations
Membrane Seperations
Ultraviolet Sterilisation

## Slide 5: Biological Tech
Digestion
Standard technology used for municipal waste treatment
Utilises micro-organisms to (an/)aerobically digest the waste components in the water
Consists of combinations of sedimenters, mixers and filters, digesters
Produces biogas (mostly methane) , liquid sludge(potential fertiliser) and water
Micro-organisms highly sensitive to environmental changes such as temperature
Reliant on living creatures for life support, increasing risk.

## Slide 6: Biological Tech
Bio-Reactor systems
Typically aerobic digestion by micro-organisms inside a CSTR reactor
Produces bio-solids which can be used for fertiliser
Sequential tanks/seperater recommeneded to reduce time to split bio-solids and treated water
Can be combined with membrane technology
Extremely Temperature Sensitive
Relying on organisms survival for life-support

## Slide 7: Biological Tech
Dark Fermentation
Produces H2,CO2, organic acids
Utilises organic wastes
Doesn’t require light
Anaerobic, aerobic or facultative bacteria can be used
Very sensitive to environmental factors including temperature, pH, ion concentrations etc
Doesn’t produce potable water as only removes approx 40% of waste components (mainly organic)

## Slide 8: Biological Tech
EcocycLET
All water retained in biomass
Not feasible

## Slide 9: Biological Tech
Bioremediation
Enzymes/Bacteria/Natural organisms consume contaminants
Similar to digestion but more specific to chemicals
Eg bacteria that break down oil spills
Maybe a bit too specific for waste water treatment

## Slide 10: Chemical Tech
Advanced Oxidation Reactions
Use hydrogen peroxide, ozone and UV to oxidise organics and non-organics in the waste water
Fast reaction rates so will be volume intensive
Can be used in batch or continuous
Reactions must be tailored for the specific waste composition
Requires input of ozone, hydrogen peroxide

## Slide 11: Chemical Tech
Electrocoagulation
Uses an electric charge to cause particles in the water to coagulate
These can then be removed in a sludge through filtration
Produces clean palatable water
Requires no chemicals added
Energy Intensive

## Slide 12: Chemical Tech
Membrane Separations
Can be used either biologically or chemically.
Membrane is designed to allow specific chemicals to permeate through it only
Can be pressure or electrical driven
Pressure - Requires no chemicals, diffusion is via concentration gradients
Electrical – electrically forces ions across the membrane leaving purified water on one side
Reverse Osmosis – Pressure driven – Most commonly used for drinking water
Nanofiltration is an emerging contender
Highly prone to fouling which reduces effectiveness
Very energy intensive
Creates a highly concentrated waste stream
Easily automated
Removes bacteria and viruses
Membranes must be replaced every 5 years

## Slide 13: Space Technologies for Water purification

## Slide 14: 4 mains types of water purification are:
ISS Baseline Technology
Vapour Phase Catalytic Ammonia Reactor (VPCAR)
Direct Osmotic Concentration (DOC)
Immobilised-cell Bioreactor (ICB)

## Slide 15: ISS System
Multistage approach to water recovery.
Lead to development of Orbital Replacement Units (ORUs), which are individual elements that can be replaced in orbit.
Process consists of multiple filtration units, volatile removal units and a quality control unit.
Urine pre-treated before entering water water feed.

## Slide 16: ISS System
Relies on non-regenerative adsorption processes, therefore high maintenance penalty (413 kg/year)
Minimal power consumption (55 Wh/kg)
High water purity received
Water recovery rate of 99%
These ORUs require regular replacement (currently working on a 90 day replacement cycle)
As there is always a shuttle every 90 days the maintenance penalty for ISS can be neglected, not the case for Mars

## Slide 17: Vapour Phase Catalytic Ammonia Reactor (VPCAR) System
Single step system that can handle all quality of waters to produce potable water
Main unit in VPCAR system is the wiped-film rotating disk evaporator. This removes undesirables from feed in a bleed stream, and evaporates the aqueous feed.
Volatiles are removed using an oxidation reactor which produces CO2, H2O and N2O.
Reducing reactor converts N2O to O2 and N2

## Slide 18: VPCAR
System is able to achieve 97% water recovery
Could be increased to 100% recovery by passing bleed stream through a lyophilizer. (freeze dryer)
Requires no regular resupply to keep running
High power requirement (312 Wh/kg)
Only has a current life span of 5 years

## Slide 19: Direct Osmotic Concentration (DOC) System
This process uses direct osmosis and osmotic distillation as a pre-treatment for reverse osmosis.
An osmotic agent (OA) is recirculated on one side of a selective membrane, and waste water on the other side.
Water travels down the concentration gradient and in dilutes the OA
Water recovered from OA using reverse osmosis.

## Slide 20: DOC System
Is able to achieve a water recovery factor in excess of 95%
Produces high quality water
Preliminary tests indicate:
  that no resupply would be required
  relatively low power consumption (102 Wh/kg)
These results still have to be tested for a longer duration

## Slide 21: Immobilised-cell Bioreactor (ICB) System
The ICB unit was responsible for organic carbon removal
A trickling filter bioreactor (TCB) follows the ICB unit which is responsible for ammonia removal.
ICB consist a cylinder with plates with equal spacing. Plates are covered with a porous polymer which supports micro-organisms.
Air enters the bottom of the cylinder to induce the upwards flow of waste water
TCB consists of a similar plate system, with micro-organism support
Reverse osmosis is performed downstream to extract purified water

## Slide 22: ICB System
Has a high power consumption of 371 Wh/kg
Not self sustaining with 119 kg/year resupply required
Potential for 100% recovery with the use of additional units

## Slide 23: Recommendations:
Further analysis into the VPCAR system and the DOC system
The main reason for this is that they both require 0kg/year resupply, in order to keep functioning
Both are able to achieve a high water recovery rate as well. 100% could be achieved by adding further units onto the system

## Slide 24: Biomass Recycling Processes
Yassen Abbas
Malcolm Chambers

## Slide 25: Growing biomass on mars
What is the best method to grow biomass on mars?
Hydroponics
Aeroponics (less water & energy required compared to hydroponics but needs more oxygen)
Soil based cropping
Soil based cropping gives an approach for waste decomposition, carbon sequestration, oxygen production and water biofiltration
Both aeroponic and hydroponic methods lose these capabilities due to lack of microorganisms.
Due to Mars's thin atmosphere, there is little protection from solar and cosmic radiation. Can we assume radiation will not penetrate the habitat?

## Slide 26: Biomass on mars
Main issue is lower gravity assuming pressure and temperature can be regulated
Effects of lower gravity:
Main consideration is on the water flow and how this changes the delivery system of nutrients.
It was found that :
Water infiltration rate substantially decreased, leading to about 90% lower water and nutrient loss by leaching
N gas emissions increased (NO (+60%), N2O (+200%) N2 (+1200%), CO2 increased by 10%)
biomass on Mars was 5–12 times higher than on Earth under terrestrial nutrient supply rates

## Slide 27: Time evolution of the soil saturation Sθ (a), pH (b), and nitrate ion concentration (c) on Earth and on Mars for depth intervals 0–5 (solid lines) and 5–10 cm (dotted lines) on Earth

## Slide 28: Waste Recycling Processes
Bo Peng
Dylan Martin

## Slide 29: Recycling Food Waste
The task proposed for each group was to create a flow-chart for the assigned resource and identify and discuss possible processes which could be used for recycling purposes.
The team task proposed was to combine potential processes to create basic BFDs for the Mars station.

## Slide 30: JAXA System
http://www.jaxa.jp/article/special/eco/oguchi_e.html

## Slide 31: JAXA System
Developed by JAXA (Japanese Aerospace Exploration Agency)
  Waste water and food waste are mixed in a sealed container.
  Air is added, then whole container is exposed to high heat and pressure.
  50% of waste is decomposed to produce ammonia and acetic acid.
  Catalyst used in catalytic converter (e.g. platinum) is added.
  Water and carbon dioxide are generated.
  Water is clear, colourless and residue free.
  Water can be used as plant fertilizer (contains inorganic components).
  If filtered, water can become potable.

## Slide 32: Thermophilic Composting-Rutgers Strategy
Combining food waste, inedible waste and faecal matter. Heat treatment at 55-60°C is needed to remove hazardous pathogens.
Thermophilic composting, properly done, can reach these sterilizing temperatures without the addition of externally supplied heat.
  The processes which generate the heat consume oxygen.
  However, it is more effective to remove heat by thermostatically controlled ventilation to ensure that maximum temperatures do not exceed 60°C than to attempt to maintain a correct oxygen level within the compost.
This method is the Rutgers Strategy. An ideal fertilizer use on Mars would be for mushroom growing, due to low light and temperature requirements.
www.4frontierscorp.com/dev/assets/MarsSettlementWRS.ppt
www.nepis.epa.gov

## Slide 33: Urine Waste Treatment in Space Ship
Distillation
1.1 Vapor Compression Distillation (VCD)
1.2 Thermoelectric Integrated Membrane Evaporation (TIME)
1.3 Air Evaporation system (AES)
2. Advance Oxidation
2.1 Vapor Phase Catalytic Ammonia Removal (VPCAR)
2.2 Supercritical Water Oxidation (SCWO)
Lyophilization
4. Biological Water Reclamation System

## Slide 34: Vapor Compression Distillation
condenser
evaporator
Steam
latent heat
Waster water inlet
Waster water outlet
Clean water outlet
Rotary compressor
Vapor compression distillation is a spontaneous process, easy to control
Urine is evaporated at the temperature which is slightly higher than surroundings, the outlet water quality is good
3. Too many moving elements lead to a negative effect on reliability

## Slide 35: Thermoelectric Integrated Membrane Evaporation
Urine inlet
preprocessor
Storage tank
Circulating tank
Thermoelectric heat pump
Heater
1. Urine will be pre-heated to 65.5°C by heater. The steam partial pressure difference between the 2 sides of membrane evaporate water on the outside surface of membrane and the steam is condensed on the cold plate. Latent heat of condensation will be transferred from the cold plate to the heater. 2/3 latent heat can be recycled.
Porous cold plate
micro-filter
Clean water
Steam
Hollow-fiber membrane evaporator
2. Little moving elements cause high reliability, easy to install. The diameter of porous of membrane is too small, it is easy to clog up by impurity.
3. Second generation increase the length of membrane and decrease the number of connectors to prevent the urine leaking problems

## Slide 36: Air Evaporation system
Condenser
Urine is evaporated after adsorbing the heat of dry hot air from the heater, the steam product will be captured by air and then transport through cooling water HX and gas/liquid separator one by one. Condensed steam goes out the system as clean water and air goes back to the heater.
This system includes simply structure, good gas-liquid separate performance, recycle rate of water can nearly meet 100%
Compressor
Heater
HX
Condenser
gas-liquid separator
Blower
Air evaporator
Activated carbon filter
Urine inlet
3. Operating under atmosphere pressure, no vacuum leaking problem. However, urine is evaporated at relatively high temperature lead to bad quality of outlet water.

## Slide 37: Vapor Phase Catalytic Ammonia Removal
HX
Ideally, this system will catalytic oxidize ammonia and some other volatile hydrocarbons which are produced during the urine evaporation process to harmless gas products. The reactions which happens in the oxidation reactor are shown below:
HX
Condenser
Evaporator
Oxidation reactor
Reduction reactor
HX
Compressor
Pump
Gas collection
O2
Exudation
Clean water
Uncondensed gases will go into the reduction reactor. Final gas products only have CO2, N2 and H2O

## Slide 38: Supercritical Water Oxidation
Water can dissolve organic and some of gases under the supercritical state (Tc = 374。C and Pc = 22MPa). This method mainly use this characteristic to transfer the organic in the urine to harmless gases such as N2, H2O and CO2 under high temperature and high pressure with catalyst operating condition.
Advantages: 1. This system has simple structure and high treatment efficiency.
2. Total reaction time is short.
Disadvantages: 1. Low reliability
2. Equipments are easy to be eroded and clogged up.
3. Process consume too much energy and Oxygen.

## Slide 39: Lyophilization
Use lyophilizer to freeze the urine sample for 14-24h at the operating condition of 19。C and 0-2Pa. And then use -55。C cold plate to collect the moisture which sublime from the ice. This process can recycle approximately 98% water. It is a self-sufficiency process which nearly consume none energy.
On the other hand, the treatment efficiency is terribly low and no further developed until nowadays.

## Slide 40: Biological Water Reclamation System
It is a well developed method of city sewage treatment but it is still in its early stage of recycle urine in space station.
Urease catalytic hydrolyze urea in the urease bed and produce CO2, NH3, NH4+,HCO3- and other ion products. These ion products will be removed by multilevel ion exchange medium. The flow in the system is ideal slug flow, operated under normal temperature. This system has stable properties and consume less energy.
Enzyme activity is affected by the concentration of iodine and the value of PH. The decomposition velocity of the urea is affected by the liquid salinity, so it is necessary to do some pretreatments such as adjust PH and remove salt and iodine. These lead to the system difficult to operate.
Positive-negative ions exchange bed
Urease bed
Positive-ions exchange bed
Positive-negative ions exchange bed
Iodation resin bed
Inlet
Outlet

## Slide 41
Project | VCDS | TIMES | AES | VPCAR
Operating condition | Approximate 25。C Vacuum | Relative high temperature Vacuum | High temperature Normal pressure | High temperature Approximate vacuum
Coefficient of recovery | 93.0% | 90.0% | Approximate 100% | 97%
Treatment effectiveness | Excellent | Good | Bad | Excellent
Energy consumption | Lower medium | Upper medium | High | High
Area | Lower medium | Small | Lower medium | Upper medium
Weight of equipment | Lower medium | Lower medium | Lower medium | Upper medium
Outgrowth | Strong liquid | Strong liquid | Impurity | Gas
Reliability | Upper medium | Upper medium | High | High
System running | Simple | Simple | Simple | Upper medium

## Slide 42
Project | SCWO | BWRS | UBR | Lyophilization
Operating condition | High temperature and pressure Oxygen required | Normal temperature Oxygen required | Normal temperature | Low temperature Vacuum
Coefficient of recovery | -- | Approximate 100% | Approximate 100% | 98%
Treatment effectiveness | Upper medium | Medium | Medium | Good
Energy consumption | High | Low | Low | Low
Area | Upper medium | Large | Large | Upper medium
Weight of equipment | Upper medium | Heavy | Heavy | Lower Medium
Outgrowth | Gas | Gas | Gas | Strong liquid
Reliability | Lower medium | Low | Low | High
System running | Upper medium | Complex | Complex | Simple

## Slide 43: Material Waste
Material waste management for future long-duration missions requires consideration of:
Paper, Tape, Hygiene Products, and Clothing
Medicines
Equipments consumption (Including filter, catalysts and accessories replacement)

## Slide 44: Thermal Recycling Processes
Lois Doig
James Young

## Slide 45: Note on Thermal Energy System
The station is assumed to have high levels of insulation, like the international space station, meaning it can be considered (for now) to be perfectly insulated.
The effects of solar radiation, therefore, are negligible.
Temperatures in the station are only dependent on the energy systems within.

## Slide 46: Reasoning Behind Thermal Recycling
Nuclear reactor is considered an unlimited energy resource. However, there are advantages to minimising energy usage:
- leaves more energy for charging batteries of vehicles
- leaves the possibility to expand the station without adding another nuclear generator
- good engineering practice

## Slide 47: Heat Exchangers in Hanford Report
AAA (avionic air assembly) provides air cooling for the equipment. Heat is removed from the FDS (fire detection & suppression) and transferred to radiators.
CCAA (common cabin air assemblies) used to cool, dehumidify and circulate the cabin air. Heat (and water) removed as condensate and stored in condensate tank.

## Slide 48: Unaddressed Thermal Processes
Exothermic Processes
Oxygen Generation Assembly
Fire Detection and Suppression
Oxygen Generation Assembly
(WGS shift)
Refrigeration
Endothermic
(Sabatier)
Water for hygiene
Laundry water
Internal radiators
Notes: Brackets here are because we haven’t finalised what method of air recycling we’re going to use.

## Slide 49: Recommendations
A thermal recycling system should be set up between some (or all) of these processes to minimise energy losses.
Any excess heat should be removed via ammonia

## Slide 50: Methods of Removing Excess Heat
If the heat generated within the station is found to be too great, it can be removed using a TCS (thermal control subsystem).
Heat is removed by water and transferred to ammonia in a heat exchanger.
Ammonia is pumped outside the station where it transfers energy to space (low m.p. of NH3 means it does not freeze)
Radiators are “anti-sun tracking radiators with Z-93 surface coating”
Notes: Q: How does the water remove heat? In radiator-type plates? Z-93 is a zinc-heavy white paint (reflects sunlight)

## Slide 51: Air Recycling Processes
Charly Raymond
Jamie Cassels

## Slide 52: General Cycle
Oxygen
Human Respiration
Carbon Dioxide
Some CO2 Reducing Process
Water
Electrolysis

## Slide 53: Possible Processes
Sabatier Reaction
Reverse Water Gas Shift Reaction
Bosch Reaction
Advantages?
Disadvantages?
Uses of byproducts

## Slide 54: Sabatier Reaction
CO2 + 4H2  CH4 + 2H2O
High temp (~400˚C)and pressure needed.
Nickel catalyst (or ruthenium on alumina)
By-product : Methane – can be used for fuel on the surface of mars
Being researched for ISS

## Slide 55: Reverse Water Gas Shift Reaction
CO2 + H2  CO + H2O
High temp (~350˚C needed)
Silica catalyst (with 5%wt Copper)
By-product: Carbon Monoxide – can be further processed into methane, methanol etc.

## Slide 56: Bosch Reaction
CO2 + 2H2 → C + 2H2O
Higher temp needed than for Sabatier and RWGS (~530-730˚C) – problems associated with maintaining this high temperature
Completely closed O2 and H2 recycle
Iron catalyst
By-product: elemental carbon – not useful – can foul catalyst surface – reduction in efficiency

## Slide 57: Electrolysis of Water
To produce O2
2H2O  2H2 + O2
Sabatier and Electrolysis
1 mol CO2
4 mol H2
1 mol O2
2 mol H2
RWGS and Electrolysis
1 mol CO2
1 mol H2
½ mol O2
1 mol H2
Bosch and Electrolysis
1 mol CO2
2 mol H2
1 mol O2
2 mol H2

## Slide 58: Replenishment Needs
Bosch: Completely closed O2 and H2 recycle
Sabatier: Loss of Hydrogen – through methane
RWGS: Loss of Oxygen – through carbon monoxide
Either will need to be replenished.
  Through electrolysis of water or from shuttle.
  H2 is lighter  cheaper to transport from Earth regularly

## Slide 59: Food Recycling Processes
Scott Clark
Sam Jones

## Slide 60
Crew Members
Waste Recycling
Food
Bodily Waste
Packaging
Bio-degradable Packaging
Food Cycle
Food that is consumed is converted into other forms, e.g. heat/work/body-mass and therefore cannot be conserved.

## Slide 61: Food requirement
Based on earth calorific requirement of approx. 2500 calories per day
Total calorie content of food required for 18 months (548 days) is approximately 13700 kcal
This calorific requirement corresponds to 57.3 MJ of energy.
How do we convert from energy to weight terms of food required?
How large a safety buffer should be included assuming possibility of resupply delay?

## Slide 62: Food Form
Fresh, Dehydrated, Shelf Stable and Frozen foods will all be sent to supply this energy to the crew members.
This means the weight of food sent up cannot be calculated until the volume of each food form has been calculated.
Sending up food in different forms adds additional weight to resupply mission due to food storage methods.
Dehydrated foods will be sent in bio-degradable packaging that can be added to the biomass

## Slide 63: ISS solution
Requirement calculation*
  For women:
  BEE = 655 + (9.6 x W) + (1.7 x H) - (4.7 x A)
  For men,
  BEE = 66 + (13.7 x W) + (5 x H) - (6.8 x A)
  Where:
  W = weight in kilograms, H = height in centimeters, and A = age in years.
Food Form
  Food planned for SS will be frozen, refrigerated, or thermo-stabilized and will not require the addition of water before consumption.
  Many of the beverages will be in the dehydrated form.
  Food will be heated to serving temperature in a microwave/forced air convection oven. One oven will be supplied for each group of 4 astronauts.
  The SS food system consists of 3 different supplies of food; Daily Menu, Safe Haven, and Extra Vehicular Activity (EVA) food.
      The Safe Haven food system is provided to sustain crewmembers for 22 days under emergency operating conditions resulting from an on-board failure.
      EVA food consisting of food and drink for 8 hours (500 calories of food, and 38 oz. of water) will be available for use by a crewmember during each EVA activity.
*From NASA Education website: http://www.nasa.gov/audience/forstudents/postsecondary/features/F_Food_for_Space_Flight.html

## Slide 64: Further Questions
How can the weight of food packaging be both calculated and minimised?
How to dispose of non-recyclable (bio-degradable) packaging?